TO:		Prospective Bidders

FROM: 	Claflin Fire District #1

DATE: 	May 1, 2018

RE: 		CLAFLIN FIRE DISTRICT #1 REQUEST FOR PROPOSAL

Claflin Fire District #1 is accepting proposals for 3 sizes of steel buildings plus options.

BUILDING 1

46x40x14 with three (3) 12x12 garage doors.  One (1) walk-in door.

BUILDING 2

60x40x14 with four (4) 12x12 garage doors.  One (1) walk-in door.

BUILDING 3

60x45x14 with four (4) 12x12 garage doors.  One (1) walk-in door.

(See attached not to scale drawings)

ALL OF THE ABOVE BUILDINGS SHALL MEET THE FOLLOWING SPECIFICATIONS:

Walls – 26 gauge – color

Roof – 26 gauge – no color – galvanized

4” white faced fiberglass insulation for the walls and roof

8’ tall metal liner on the interior wall white in color

Steel overhead doors – insulated – electric operators – with wall buttons and remote visor buttons – 3 – 24” x 5” windows

1 Steel walk-in door – solid panel – push button coded lockset – closer

No windows

Base trim, gable trim, and eave trim

Rain gutter installed above garage doors with appropriate placement and number of down spouts

Concrete:

8”x30” reinforced concrete foundation with reinforced concrete piers as required.

6” reinforced (paving mesh on “chairs”) sealed concrete floor with a total of 4” slope from rear to front of building.  Plumbing for sewer and water line to be installed prior to concrete being poured.

There shall be a minimum 4” stem wall along the rear of the building.  The stem wall sides shall match the rear at that point and increase as the floor slopes towards the garage doors.

10’ x building length x 6” reinforced concrete approach in front of the overhead doors.

Bollard pipes on either side of each overhead door to protect the openings.

Freight

Erection

ELECTRICAL

Contractor will seek and submit proposals, and include in the bid, for materials and installation of 100 amp service entrance with a disconnect, breaker box, wiring for garage door openers, electrical outlets, lighting, heater and light switches.

Lighting will be LED with six (6) four foot 4 bulb fixtures, one (1) “wall-pack” dusk to dawn light fixture on the outside front/middle of the building.  Inside outlets will include two (2) wall outlets on the back wall, one (1) on each end of the building, one (1) outlet near the walk-in door and four (4) outlets on the front of the building one (1) between each overhead door.  One (1) outlet on the outside of the building between the two middle overhead doors.

HEATING

Contractor will seek and submit proposals, and include in the bid, for a heater and installation.  Installation will include gas service from the heater to the meter including the “shut-in” test.

Heating will be either one (1) “overhead” heater or a “radiant” heater of approximately 150,000 BTUs.

SITE PREPARATION

Contractor will seek and submit proposals, and include in the bid, for necessary elevation and grade leveling/preparation of the building.

TIMING

Contractor will provide an estimated project start date and must provide a ten (10) day notice of expected arrival time for commencement of contract.  The completion date should be no later than September 15, 2018.

TERMS

Contractor’s payment schedule approved with Fire District acceptance of project.

STORAGE OF MATERIAL AND EQUIPMENT

Contractor may store equipment and material necessary for the project on the Eastern portion of the Fire District’s property located at 309 West Front Street in Claflin i.e. site of the building project.

CERTIFICATE OF INSURANCE AND BOND

Contractor will submit all required statutory payment and warranty bonds for the entire contract amount before any work begins, also proof of statutory cover of workman’s compensation for contractor and any subcontractors and contractors liability insurance.  Contractor shall be able to provide a performance bond or other satisfactory guarantee of performance.

Contractor will be responsible for all applicable permits.

PROPOSAL FORM

Contractor shall provide, upon company stationary, information requested within the proposal form.  Included shall be prices.  Provided shall also be an estimate of time necessary for the completion of the project.  Fire District #1 is exempt from State and Local Sales Taxes.

Proposals shall be returned no later than 3:00 p.m., May 21, 2018 in a sealed envelope marked “2018 Claflin Fire District #1 Building Proposal”.  Awarding of the contract is expected to be June 4, 2018 by the Barton County Commission at the regular meeting on that day.  The Fire District reserves the right to accept or reject any or all proposals.

Bids shall be submitted to:

Claflin Fire District #1

C/O Barton County Clerk/Room 202

County Court House

1400 N Main

Great Bend, KS 67530

Claflin Fire District #1 reserves the right to reject any and all bids and to waive irregularities.  In the case of ambiguity or lack of clearness in stating the specifications, the Fire District reserves the right to waive irregularities or reject the bid.

Sealed bids are due on May 21, 2018 at 3:00 p.m.